## Slide 1: Mesh Network of Realtek
2013/10/09

## Slide 2: Outline
What is Mesh?
Mesh Protocol Introduction
Compiler Configuration
Mesh GUI
Mesh Demo I
Mesh Demo II

## Slide 3: What’s Mesh? – Overview
The entire wireless mesh cloud be treated as a single (giant) Ethernet switch
Simple, fast installation
  Where wires are not desired (e.g., hotels, airports)
  Where wires are impossible (e.g., historic buildings)
Internet

## Slide 4: What’s Mesh? – Mesh vs. Repeater
Auto Connect
  A mesh node can automatically scan nearby mesh nodes and join the mesh network without further configuration
    More convenient to install
    Extensible
Repeater
ADSL
Mesh
ADSL
D
C
B
A
A
D
C
B

## Slide 5: What’s Mesh? – Mesh vs. Repeater (cont.)
Path Recovery
  Once some error occurs on some mesh node, the mesh network can find another routing path to the destination.
    More robust
    No single point of failure
Repeater
ADSL
D
A
C
B
Mesh
ADSL
A
D
C
B

## Slide 6: What’s Mesh? - Topology

## Slide 7: What’s Mesh? - Terminology
Mesh Point (MP)
  A station (STA) that implements the mesh facility. A mesh STA that operates in the mesh BSS (MBSS) may provide the distribution services for other mesh STAs.
Mesh Access Point (MAP)
  A mesh station that is collocated with one or more access point(s).
Proxy Mesh Station (Portal, MPP)
  A mesh STA that represents 802 entities outside the mesh basic service set (MBSS).
Peering
  A logical relationship from one mesh STA to another mesh STA that has been established with the mesh peering management (MPM) protocol
Mesh Gate
  A mesh station that has access to external STAs (STAs outside MBSS) called a Mesh Gate. Both MAP and MPP are Mesh Gates

## Slide 8: Mesh Protocol Intro. – Discovering & Peering
Mesh nodes discover its one-hop neighbors through passive or active scan, that is listening Beacon or transmit Probe Req.
Compare mesh profile (Mesh ID), data rate, mesh capability, etc in Beacon or Probe Rsp to find candidate peer mesh STA.
Mesh nodes become “peer” (or “neighbor”) to each other through mutual association.
Each mesh nodes maintains a neighbor table
Mesh nodes can only transmit data through “neighbor”
A
C
B
E
S
B
E
B
C
D
S
B
A
C
D
E
S
C
E
D
B
A

## Slide 9: Mesh Protocol Intro. – HWMP
Mesh path selection protocol - Hybrid Wireless Mesh Protocol (HWMP).
  Proactive tree building mode
    Gate announcement (GANN)
  On demand mode (AODV)
    Path request (PREQ)
    Path reply (PREP)
    Path error (PERR)
Each mesh node maintains a routing table, in which contains forwarding information: {destination MAC, next-hop MAC, metrics, …}

## Slide 10: Mesh Protocol Intro. – HWMP(cont.)
GANN
  Used to announce the presence of the mesh gate.
  Mesh gate broadcast GANN for every 3 second.
S
A
2
3
3
3
1
dst | next | metric
S | S | 2
dst | next | metric
S | S | 3
dst | next | metric
S | A | 5
dst | next | metric
S | C | 6
dst | next | metric
S | S | 2
dst | next | metric
S | S | 3
dst | next | metric
S | C | 6
dst | next | metric
S | C | 4
5
2
2
dst | next | metric
S | E | 8
dst | next | metric
S | C | 4
dst | next | metric
S | B | 6
D
E
C
B

## Slide 11: Mesh Protocol Intro. – HWMP(cont.)
dst | next | metric
A | B | 4
B | C | 1
D | B | 3
E | E | 3
S | S | 3
dst | next | metric
C | C | 1
A | A | 3
D | D | 2
E | D | 4
S | C | 4
dst | next | metric
C | C | 3
B | C | 4
D | C | 6
E | C | 6
A | A | 2
dst | next | metric
C | B | 4
B | B | 3
D | B | 5
E | B | 7
S | S | 2
dst | next | metric
C | C | 3
B | D | 4
D | D | 2
A | C | 7
S | C | 6
dst | next | metric
C | B | 3
B | B | 2
A | B | 5
E | E | 7
S | B | 6
S
A
2
3
3
3
1
B
5
2
2
D
E
C

## Slide 12: Mesh Protocol Intro. – HWMP(cont.)
AODV
  Source node broadcast a PREQ frame flooding to all mesh nodes
  Ever PREQ received, mesh node(s) create a reverse path to source
  When some mesh node knows destination, reply unicast PREP to source mesh node
S
A
B
D
E
C
PREQ
PREQ
PREQ
PREQ
PREQ
PREQ
PREQ
PREQ
PREP
PREP
PREP

## Slide 13: Mesh Protocol Intro. – Interworking with the DS
When two STAs behind mesh gates (external STA ) need to communicate with each other.
Each mesh gate maintains a proxy table, in which contains proxy information { external STA’s address, proxy mesh gate’s address, …}
If the proxy information does not exist, do AODV first.
These proxy information is carried by PREP, or PUX (proxy update) packet.
S
B
D
E
C
STA1
STA2
PREP
PREP
PREP
Mesh gate
Mesh gate
sta | owner
STA2 | D
sta | owner
STA2 | D
sta | owner
STA2 | D
A
PREQ
PREQ
PREQ
PREQ
PREQ
PREQ
PREQ
PREQ

## Slide 14: Data Forwarding – Address transform
Ref. proxy table

## Slide 15: Compiler Configuration – Select Board

## Slide 16: Compiler Configuration – Config Kernel
Device Drivers -> Network device support -> Wireless LAN

## Slide 17: Compiler Configuration – Config Users

## Slide 18: Mesh GUI – Mesh Setup

## Slide 19: Mesh GUI – Mesh Setup (cont.)

## Slide 20: Mesh GUI – Mesh Information
c2
c1
c3
c4

## Slide 21: Mesh GUI – Mesh Information (cont.)

## Slide 22: Mesh DEMO I
Auto Connect
1. Power on MAP1 and connect STA1 to it (Ethernet)
2. After the MAP1 has chosen an available channel, power on the other three MAPs
3. Connect STA2 to MAP4 (wireless)
4. Ping all MAPs and STA2 from STA1
MAP1
STA1
STA2
MAP4
MAP2
MAP3
Ping
ACL Denied

## Slide 23: Mesh DEMO II
Path Recovery
1. Power off MAP2
2. Check if STA1 can communicate with STA2
3. Power on MAP2 again
4. Check if the routing path from MAP1 to MAP4 has changed from MAP1-MAP3-MAP4 to MAP1-MAP2-MAP4
MAP4
MAP2
MAP3
MAP1
STA2
STA1
Ping
Ping
ACL Denied